## Slide 1: Radio Receivers
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 2: EC 326 COMMUNICATION SYSTEMS UNIT – I Part II
T Srinivasa Rao
Dept. of ECE
Bapatla Engineering College
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 3: Main Functions
Intercept the electromagnetic waves in the receiving antenna to produce the desired R.F. modulated carrier.
Select the desired signal and reject the unwanted signals.
Amplify the R.F. signal
Detect the RF carrier to get back the original modulation frequency voltage .
Amplify the modulation frequency voltage.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 4: Classification
AM. (Amplitude Modulation) Broadcast Receivers.
F.M. (Frequency Modulation) Boadcast Receivers.
T.V. (Television) Receiver.
Communication Receivers.
Code Receivers.
Radar Receivers.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 5: Features
Simplicity of operation.
Good Fidelity.
Good Selectivity.
Average Sensitivity.
Adaptability to different types of Aerials.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 6: A M Receivers
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 7: Basic Functions of A M Receivers
Reception.
Selection.
Detection.
Reproduction.
Straight Receivers
Superheterodyne Receiver.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 8
Noncoherent Tuned Radio-Frequency Receiver
Audio detector
Audio amplifier
RF amp.
RF amp.
RF amp.
Antenna coupling network
Difficult to tune
Q remains constant  filter bandwidth varies
Nonuniform selectivity
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 9: ?
For an AM receiver commercial broad cast band receiver (535KHz to 1.605MHz) with an input filter Q factor of 54 , determine the bandwidth at the low and high ends of RF spectrum
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 10
Band width at low frequency
Band width at high frequency
-3dB band width at low frequency is 10KHz but at high frequency 3 times that of the low frequencies.
Tuning at high end of the spectrum three stations would be received simultaneously.
To achieve band width of 10KHz at high frequencies a Q of 160dB is required but with a Q of 160 the band width at low frequencies is
It is too selective and band rejection will takes place.
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 11
Pre
selector
RF
amplifier
Mixer
IF
Amplifier
Band pass
filter
AM
Detector
Audio
Amplifier
Local
Oscillator
Mixer / Converter
Section
RF Section
IF Section
Audio detector Section
Audio amplifier Section
speaker
Gang tuning
RF signal
IF signal
Audio Frequencies
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 12
TRF - non uniform selective
Heterodyne receiver
Gain
Selectivity
Sensitivity
Heterodyne
Mix two frequencies together in a non linear device.
Translate one frequency to another using non linear mixing
Heterodyne receiver has five sections
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 13
RF section
IF section
Mixer / converter section
Audio detector Section
Audio amplifier Section
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 14
RF Section
Pre-selector
Amplifier stage
Broad tuned band pass filter with adjustable frequency that is tuned to carrier frequency
Provide initial band limiting to prevent specific unwanted radio frequency called image frequency from entering into receiver.
Reduces the noise bandwidth of the receiver and provides the initial step toward reducing the over all receiver bandwidth to the minimum bandwidth required to pass the information signal.
It determines the sensitivity of the receiver.
RF amplifier is the first active device in the network it is the primary contributor to the noise. And it is the predominant factor in determining the noise figure.
Receiver may have one or more RF amplifier depending on the desired sensitivity.
Due to RF amplifier
Greater gain and better sensitivity
Improved image frequency rejection
Better signal to noise ratio
Better selectivity.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 15: RF Amplifier
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 16
Demodulation process:
High frequency signal
Frequency translation
RF  IF
IF source information
RF for commercial broadcast purpose
AM broadcast band
535 – 1605 KHz and IF 450 – 460 KHz.
FM broadcast band
88 – 108 MHz and IF 10.7MHz
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 17
Local oscillator
Mixer
Mixer stage is a nonlinear device
Convert radio frequencies to intermediate frequency
Radio frequencies are down converted to intermediate frequency
Heterodyning takes place in the mixer stage.
Carrier and sidebands are translated to high frequencies without effecting the envelope of message signal.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 18
Frequency conversion
Similar to that of modulator stage
Frequencies are down converted.
Frequency conversion
The difference between the Rf and Local oscillator frequency is always constant IF
The adjustment for the center frequency of the preselector and the adjustment for local oscillator are gang tuned.
The two adjustments are mechanically tied together and single adjustment will change the center frequency of the pre selector and the local oscillator
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 19
Local oscillator frequency is tuned above RF
High side injection
Low side injection
Local oscillator frequency is tuned below RF
f LO = fRf + fIF
f LO = fRf - fIF
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 20
RF-to-IF conversion
Preselector
535 - 565 kHz
Mixer
IF filter
450 – 460 kHz
Oscillator
1005 kHz
Receiver RF input (535 – 1605 kHz)
565 kHz
535
545
555
470 kHz
440
450
460
450
460 kHz
IF Filter output
high-side injection (fLO > fRF)
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 21: Frequency Mixer and Oscillator
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 22: Frequency Conversion
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 23
535
540
545
550
555
560
565
440
445
450
455
460
465
470
Channel 1
Channel 2
Channel 3
450
455
460
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 24
For an AM super heterodyne receiver that uses high side injection and has a local oscillator frequency of 1355KHz determine the IF carrier upper side frequency, and lower side frequency for an RF wave that is made up of a carrier and upper and lower side bands 900 and 905 and 895KHz respectively
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 25
Pre
selector
RF
amplifier
IF
Amplifier
Band pass
filter
Mixer / Converter
Section
RF Section
IF Section
Local oscillator
Ganged tuning
455 460
In KHz ch-2
895 900 905
In KHz ch-2
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 26
LOCAL OSCILLATOR TRACKING:
TRACKING:
It is the ability of the local oscillator in a receiver to oscillate either above or below the selected radio frequency carrier by an amount equal to the IF frequency through the entire radio frequency band.
High side injection: Local oscillator frequency frf+fif
Low side injection: Local oscillator frequency frf-fif
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 27: Tracking
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 28
Ls
Lp
Ct
Co
Co
Ct
Lp
Lp
Ls
Preselector
Tuned circuit
Preselector
RF output
LO output frequency
Local oscillator tuned circuit
Gang tuning
Poor tracking
Ideal tracking
Three point tracking
600 800 1000 1200 1400 1600
PRESELECTOR AND LOCAL OSCILLATOR
TRACKING CURVE
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 29
The tuned ckt in the preselector is tunable from the center frequency from 540KHz to 1600 KHz and local oscillator from 995KHz to 2055KHz.( 2.96 to 1)
Tracking error: the difference between the actual local oscillator frequency to the desired frequency.
The maximum tracking error 3KHz + or -.
Tracking error can be reduced by using three point tracking.
The preselector and local oscillator each have trimmer capacitor ct in parallel with primary tuning capacitor co that compensates for minor tracking errors in the high end of AM spectrum.
The local oscillator has additional padder capacitor cp in series with the tuning coil that compensates for minor tracking errors at the low end of AM spectrum.
With three point tracking the tracking error can be adjusted from 0Hz at approximately 600KHz, 950KHz AND 1500KHz
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 30
Image frequency :
It is any frequency other than the selected radio frequency carrier that is allowed to enter into the receiver and mix with the local oscillator will produce cross product frequencies that is equal to the intermediate frequency.
flo =fsi+fif → fsi=flo-fif when signal frequency is mixed with oscillator frequency one of the by products is the difference frequency which is passed to the amplifier in the IF stage.
The frequency fim= flo+fsi the image frequency will also produce fsi when mixed with fo .
For better image frequency rejection a high IF is preferred.
If intermediate frequency is high it is very difficult to design stable amplifiers.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 31
LO
RF
SF
IF
IM
fif
fif
2fif
frequency
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 32
Image frequency rejection ratio
It is the numerical measure of the ability of the preselector to reject the image frequency.
Single tuned amplifier the ratio of the gain at the desired RF to the gain at the image frequency.
If multiple amplifiers are there the IFRR is nothing but the product of IFRRs of the individual stages.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 33: ?
In a broadcast superheterodyne receiver having no RF amplifier, the loaded Q of the antenna coupling circuit (at the input of the mixer ) is 100. If the intermediate frequency is 455kHz, calculate the image frequency and its rejection ratio at(a) 1000 kHz and (b) 25 MHz.
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 34
For an AM broad cast band super heterodyne receiver with If, RF, LO frequencies are 455KHz, 600KHz, 1055KHz determine
Image frequency
IFRR for a preselector Q of 100
Fim = flo+fif
Fim = frf+2fif
Fim= 1510 kHz.
ρ= 2.113
IFRR= 211.3
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 35
For citizens band receiver using high side injection with an RF carrier of 27MHZ and IF center frequency of 455KHz determine
LO frequency
Image frequency
IFRR for a preselector Q of 100
Preselector Q required to achieve the same IFRR as that achieved for an RF carrier of 600KHz input.
Ans:
27.455MHz
27.91MHz
6.77
3167.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 36
Double spotting : it occurs when the receiver picks up the same station at two near by points on the receiver tuning dial.
It is caused by poor front end selectivity and inadequate image frequency rejection.
Weak stations are overshadowed.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 37: Choice of IF : Factors
If the IF is too high
Poor Selectivity and Poor adjacent channel rejection.
Tracking Difficulties.
If the IF is too low
Image frequency rejection becomes poorer.
Selectivity too sharp and cutting off sidebands
Instability of oscillator will occur.
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 38: Frequencies Used
Standard broadcast AM : 455 kHz (465 kHz).
AM,SSB ( shortwave reception ) is about 1.6 -2.3 MHz
FM (88-108 MHz): 10.7 MHz.
Television Rx: ( VHF band 54-223MHz and UHF band 470-940 MHz): Between 26 and 46 MHz.
Microwave and RADAR ( 1-10GHz): 30,60,70MHz.
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 39: IF AMPLIFIER
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 40: Detector and AVC
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 41: Tone Compensation Volume Control
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 42: Detector using Transistor
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 43: Tone Control
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 44: Tuning Control
T Srinivasa Rao
<number>
Communication Systems ( EC-326)

## Slide 45
IF
RF
LO
Image
455 kHz
600
1510
1055
IFRR = 211.3  Q (600 kHz) = 100 (Simple preselector)
Low Q
Example
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 46
IF
RF
LO
Image
455 kHz
600
1510
1055
RF
Image
LO
27 MHz
27.455
27.91
IFRR = 211.3  Q (27 MHz) = 3167 Q (600 kHz) = 100
High Q
Low Q
Example
Solution: Use higher IF frequencies
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 47
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 48
Gain and Loss
Preselector
RF amplifier
Mixer
Bandpass filter
IF amplifier
Audio detector
Audio amplifier
oscillator
RF-section
IF-section
Use dB !!!
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 49
Envelope detector or Peak detector
IF-in
Audio out
C
R
D
?
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 50
Envelope detection
IF-in
Audio out
C
R
D
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 51
Envelope detection
for m=70.7%
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 52
Receiver Parameters
Selectivity
Bandwidth Improvement
Sensitivity
Dynamic Range
Fidelity
Insertion Loss
Noise Temperature
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 53
SQUELCH CIRCUITS
The purpose of the squelch circuit is to quite the receiver in the absence of the received signal.
The AM receiver is tuned to a location in the RF spectrum where there is no RF signal. The AGC circuit is adjust the receiver for a maximum gain.
The receiver amplifies and demodulates the noise signal.
Crackling and sputtering sound heard in the speaker in the absence of RF signal.
Each station is continuously transmitting carrier regardless of the no modulating signal.
The only time the idle receiver noise is heard is when tuning is between stations.
A squelch circuit keeps the audio section of the receiver turned off in the absence of the received signal.
DISADVANTAGE : WEAK RF SIGNAL WILL NOT PRODUCE AN AUDIO OUTPUT.
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 54: F M Receivers
T Srinivasa Rao
BEC_ECE <number>
Communication Systems ( EC-326)

## Slide 55
Fm receiver is like a super heterodyne receiver.
Double conversion super heterodyne receiver
The preselector , RF amplifier first and second mixers.
If section and detector sections of FM receivers perform identical functions to that of AM receiver.
Preselector rejects he image frequency.
RF amplifier establishes the signal to noise ratio and noise figure.
The mixer down converts RF to IF .
The IF amplifier provides the most of the gain and selectivity of the amplifier.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 56
PRESELECTOR
RF AMPLIFIER
1ST MIXER
BUFFER
1ST LOCAL OSCILLATOR
BANDPASS FILTER
2ND MIXER
IF AMPLIFIER
BANDPASS FILTER
BANDPASS FILTER
LIMITER
DEMODULATOR
DEEMPHASIS NETWORK
AUDIO AMPLIFIER
BUFFER
2ND OSCILLATOR
AGC voltage
1st IF
2nd IF
Audio detector
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 57
The detector removes information from the modulated wave.
The AGC used in AM receivers and not used FM receivers because in FM there is no information contained in Amplitude.
With FM receivers a constant amplitude IF signal in to demodulator is desirable.
FM RX have mush more UIF gain than AM receivers.
The harmonics are substantially reduced by the use of band pass filter which passes only the minimum bandwidth necessary to preserve the information signal.
The If amplifiers are specially designed for ideal saturation and is called limiter.
The detector stage consists of discriminator and de-emphasis network.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 58
The discriminator extracts the information from the modulated wave.
The limiter circuit and de-emphasis network contribute to an improvement in signal to noise ratio which is achieved in audio demodulator stage of FM receivers.
brad cast FM band receivers
IF = 10.7MHz for good image frequency rejection
Second IF is at 455KHz. IF amplifier to have relatively high gain.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 59
Fm demodulators are frequency dependent circuits designed to produce an output voltage that is proportional to the instantaneous frequency at its input.
The transfer function of the circuit is Kd = V(volts) / f(Hz)
Kd transfer function
The output from the FM demodulator is given by
Vout(t) = KdΔf
Vout(t) = demodulated output signal
Kd = demodulator transfe function
Δf = difference between the input frequency and the center frequency
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 60
FM in
La
Ca
Ci
Ri
Di
-Δf fc +Δf fo
V out
Voltage vs Frequency Curve
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 61
SLOPE DETECTOR:
Slope detector is the simplest form of the tuned circuit frequency discriminator.
It has most nonlinear voltage vs frequency characteristic.
The tuned circuit La and Ca produces an output voltage that is proportional to the input frequency.
The maximum output voltage occurs at resonant frequency.
The output decreases linearly as thee input frequency increases are decreases below resonant frequency.
The circuit is designed so that the IF center frequency fc falls in the center of the most linear portion of the voltage vs frequency curve.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 62
When the IF deviates below the fc the output voltage decreases.
When the IF deviates above the fc the output voltage increases.
The tuned circuit converts the frequency variations to amplitude variations.
Di Ci Ri make up a simple peak detector that converts the amplitude varioations to an output voltage that varies at a rate equal to that of the input frequency changes and whose amplitude is proportional to the magnitude of the frequency changes.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 63
FM in
La
Ca
Ci
Ri
R2
C2
Cb
Lb
L
-Δf fc Δf
fa fb
Vout
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 64
Balanced slope detector:
A balanced slope detector has two single ended slope detectors connected in parallel.
They are fed with 180o out of phase signals.
The phase inversion is obtained by center tapping the tuned secondary windings of T1.
La and Ca & Lb and Cb perform the FM to AM conversion
The balanced peak detector D1, C1 & R1 and D2, C2, &R2 remove the information from the envelope AM.
The top tuned circuit tuned to a frequency fa that is above IF center frequency.
The bottom tuned circuit tuned to frequency fb that is below the IF center frequency by an equal amount.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 65
The output voltage from each tuned circuit is proportional to the input frequency.
The output is rectified by the diode.
The closure the input frequency is to the resonant circuit the greater the output voltage.
The IF frequency falls exactly half way between the output voltage from the two tuned circuits.
The rectified output voltage across R1 and R2 when added produce a differential output voltage Vout = 0.
When the IF deviates above resonance the top tuned circuit produce more output voltage than the bottom tuned circuit and the output goes +ve.
When the IF deviates below resonance the bottom tuned circuit produce more voltage and the output is more –ve.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 66
The slope detector is the simplest FM detector circuit it has disadvantages like
Poor linearity
Lack of precision for limiting
Difficult for tuning.
Because of limiting is not provided the slope detector produce output voltage proportional to the frequency as well amplitude.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 67
FM in
La
Co
C1
Rs
Cs
C2
Cb
Lb
L p
-Δf fc Δf 0V
fin < fo fin > fo
Vout
L3
T1
Cc
Maximum +ve output
Average +ve voltage
-
+
-
+
VLa
VLb
I p
V p
C p
Vs = Va + Vb
+
-
VL3 = Vin
I1
I2
+
-
+
-
Vout
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 68
Foster Seeley discriminator is similar to balanced slope detector.
The capacitance value Cc C1 and C2 are chosen such that they are short circuits for IF center frequency.
The right side of L3 is at ground potential and IF signal is fed directly across L3(VL3).
The incoming IF is inverted 180o by the transformer T1 and divided equally between La and Lb.
At resonant frequency of the secondary tank circuit the secondary current Is is in phase with the total secondary voltage (Vs) and 1800 out of phase with the VL3.
Because of loose coupling the primary of T1 acts as an inductor and the primary current Ip is 90o out of phase with Vin
The voltage induced in the secondary is 900 out of phase with Vin
The voltages Vla and Vlb are 1800 out of phase with each other and in quadrature 900 out of phase with Vl3.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 69
The voltage across the top diode is the vector sum of Vl3 and Vla. And the voltage across the bottom diode is the vector sum of Vl3 and Vlb.
The voltage across D1 and D2 are equal at resonance the currents I1 and I2 are equal and C1 and C2 are charged to same voltage with opposite polarity.
Vout = VC1 – VC2
When the IF goes above resonance Xl > Xc the secondary tank circuit impedance is inductive and the secondary current lags the seconadry voltage by an angle θ which is proportional to the magnitude of the frequency deviation.
When the IF goes below resonance Xl < Xc the secondary tank circuit impedance is capacitive and the secondary current leads the secondary voltage by an angle θ which is proportional to the magnitude of the frequency deviation.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 70
VD1
VLa
Vp
Vs
VD2
VLb
Is
VLa
VD2
VLb
VD1
VLa
Vp
Vs
Is
θ
θ
VD1
VLa
VD2
VLb
Vp
Vs
Is
fin = fo
fin < fo
fin > fo
VectOr diagram
fin = fo;
fin > fo;
fin < f0;
1
2
3
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 71
FM in
La
Co
Ci
Rs
Cs
C2
Cb
Lb
L p
-Δf fc Δf 0V
fin < fo fin > fo
Vout
L3
T1
Cc
Maximum +ve output
Average +ve voltage
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 72
The ratio detector is relatively immune to amplitude variations in its input signal.
A ratio detector has a single tuned circuit in the transformer secondary.
The voltage vectors for D1 and D2 are identical but the diode D2 is reverse biased.
The current Id flows along the outermost loop of the circuit.
After several cycles of the input voltage the shunt capacitor Cs approximately charged to the peak voltage across the secondary windings.
The reactance of the capacitance is low and Rs simply provides a DC path for diode current.
The time constant RsCs is sufficiently long so that rapid changes in the amplitude of the input signal due to thermal noise or other intervering signals are shorted to ground and have no effect on the average voltage across Cs.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 73
C1 and C2 charge and discharge proportional to frequency changes in the input signal and are relatively immune to amplitude variations.
At resonance the output voltage is divided equally between C1 and C2 and redistributed as the input frequency changes above or below resonance frequency.
The change in the output voltage is due to the changing ratio of the voltage across C1 and C2 while the total voltage is clamped by Cs.
The ratio detector output voltage is relatively immune to the amplitude variations it is often selected over discriminator.
The discriminator produces more linear output voltage Vs frequency.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 74
Thermal noise with constant spectral density added to FM signal produces an unwanted deviation of the carrier frequency.
The magnitude of the unwanted frequency deviation depends on the relative amplitude of the noise with respect to the carrier.
Unwanted carrier deviation is demodulated it becomes noise if it has the frequency components that fall with in the frequency components of the information frequency spectrum.
The noise voltage at the output of the PM demodulator is constant with frequency.
The voltage at the output of the FM demodulator increases linearly with frequency.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 75
The noise component Vn is separated in frequency from the signal component Vc by frequency fn.
Assume Vc > Vn
The peak phase deviation due to interfering signal frequency sinusoid occurs when the signal and noise voltages are in quadrature phase.
ΔθPeak =Vn / Vc rad.
Limiting the amplitude of the composite FM signal on noise the single frequency noise signal has been transposed into a noise sideband pair each with an amplitude Vn/2.
If these sidebands are coherent the peak phase deviation is still {Vn/Vc}
The unwanted amplitudes have been removed which in turn reduces the signal power but does not reduce the interference in the demodulated signal due to unwanted phase deviation.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 76
The instantaneous frequency deviation Δf(t) is thee first time derivative of the instantaneous phase deviation.
When the carrier component is much larger than the noise voltage the instantaneous phase deviation can be
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 77
For noise modulating frequency fn the peak frequency deviation is
Noise frequency is displaced from the carrier frequency.
Noise frequency that produces components at the high end of the modulating signal frequency spectrum more frequency deviation for the same phase deviation than the frequencies that fall at the low end.
FM demodulation that generate an output voltage that is proportional to the frequency deviation and equal to the difference between the carrier frequency and interfering signal frequency.
Therefore high frequency noise signal produces more demodulated noise than low frequency components.
The signal to noise ratio at the output of the demodulator is
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 78
The noise in FM is non-uniformly distributed.
The noise at the higher modulating signal frequencies is inherently greater than the noise at low frequencies.
Noise
 Signal Frequency Interference
 Thermal Noise
Information signal with uniform signal level a non-uniform signal to noise ratio is produced .
Higher modulating frequencies have lower signal to noise ratio than lower frequencies.
To compensate for this, high frequency modulating signals are emphasized or boosted in amplitude in the transmitter prior performing modulation.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 79
Uniform signal level
Non-Uniform noise level
S/N is maximum
S/N is minimum
Non-Uniform signal level
Non-Uniform noise level
S/N is uniform
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 80
To compensate this boost the high frequency signals are attenuated or de-emphasized in the receiver after demodulation has been performed.
De-emphasis network restores the original amplitude VS frequency characteristic of the information signal.
The pre-emphasis network allows the high frequency modulating signals to modulate the carrier at higher level and thus cause more frequency deviation than their original amplitudes.
The pre-emphasis network is a high pass filter and it provide a constant increase in the amplitude of the modulating signal with increase in the frequency.
In FM 12dB of improvement is achieved by using the pre-emphasis and de-emphasis network.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 81
Vcc
in
output
R=10KΩ
L/R=75μs
RC=75μs
L=750mH
R=75KΩ
C=1nF
in
output
+17dB
3dB
0dB
-3dB
-17dB
de-emphasis
Pre-emphasis
2.12 KHz 15KHz
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 82
The break frequency is determined by RC or L/R time constant of the network.
The break frequency occurs when Xc = XL = R.
The pre-emphasis network can be either active or passive.
The result of using passive network would be the decrease in the signal to noise ratio at lower modulating frequencies rather than increase in SNR at the higher modulating frequencies.
The output amplitude of the network increases with the frequency for frequencies above the break frequencies.
Change in the frequency of the modulating signal produce corresponding change in the amplitude and the modulation index remains constant with frequency.
<number>
T Srinivasa Rao
Communication Systems ( EC-326)

## Slide 83
With the commercial broadcast FM modulating frequencies below 2112 Hz produce frequency modulation and above would produce phase modulation.
The noise is generated internally in FM demodulators inherently increase with frequency which produces a non uniform signal to noise ratio at the output of the demodulator.
The SNR is lower for higher modulating frequencies than for the lower modulating frequencies.
By providing pre-emphasis and de-emphasis network we produce uniform signal to noise ratio at the output of the demodulator.
<number>
Communication Systems ( EC-326)
T Srinivasa Rao