## Slide 1: Radio Transmitters
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 2: EC 326 COMMUNICATION SYSTEMS UNIT – I Part I
T Srinivasa Rao
Dept. of ECE
Bapatla Engineering College

## Slide 3: Part 1
RADIO TRANSMITTERS:
Frequency allocation for radio communication systems.
Block diagrams and functions of radio transmitters for AM and FM systems.
T Srinivasa Rao
Communication Systems (EC-326)
<number>

## Slide 4: Types of Communication
Simplex – A can talk to B
Radio, T.V. broadcasting, CD/DVD ROM
Simplest type, requires one transmitter and one receiver
Duplex - A and B both can talk to each other simultaneously
Telephone, Telegraph
Complex, requires two transmitter and two receiver at both ends
Needs two different channels for simultaneous transmission
Half-Duplex – A and B can both talk to each other but not simultaneously
Fax, CD/DVD RW
Needs one single channel for transmission
Compromise between two, don’t require separate transmitter and receiver
Same antenna and circuitry may be used for both transmission and reception
A transceiver is a small unit that combines a transmitter and a receiver.
A
B
A
B
A
B
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 5: Modulation
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 6: Radio communication services
Radio broadcasting
TV broadcasting
Satellite communication
Mobile telephony
Internet
and more ....
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 7: Radio Communication
Radio Communication means any transmission, emission or reception of signs, signals, writing, images, sounds or intelligence of any nature by means of electromagnetic waves of frequencies 0Hz - 3000GHz propagated in space without artificial guide.
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 8: Radio Commun. - Building Blocks
Basically, a radio communication system consists of a transmitter, a channel, and a receiver.
In a transmitter,
The input sound signal is converted into equivalent electrical current / voltage by a transducer
The transducer output is amplified by a chain of amplifiers (so that it can travel longer distance)
The purpose of the transmit antenna is to efficiently transform the electrical signal into radiation energy
In a receiver,
The receive antenna efficiently accepts the radiated energy and convert it to an electrical signal
As the signal suffered attenuation during travel it requires further amplification
The output transducer converts the electrical signal back into sound energy
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 9: AM & FM
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 10
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 11: Frequency Spectrum used in Radio Communications
Name | Frequency Range | Wave Length | Application | Propagation
ELF | 300Hz - 3kHz | 100 km - 1000km | Navigation, long distance communication with ships | Wave tube between earth surface and the ionosphere
VLF | 3kHz - 30kHz | 10Km-100Km | Navigation, long distance communication with ships | Ground propagation, stable
LF | 30kHz - 300kHz | 1Km-10Km | Navigation, long distance communication with ships | Ground propagation, stable
MF | 300kHz - 3MHz | 100m-1Km | AM broadcasting, radio navigation Ship to Shore Comm’n. | Ground-wave, sky-wave propagation. Fading
HF | 3MHz - 30MHz | 10m-100m | National and International Broadcast; Point to point telephone and telegraph Comm’n. | Large perturbation, reflection in ionosphere
VHF | 30MHz - 300MHz | 1m-10m | Radio and TV broadcasting, FM Broadcast, Short distant Comm’n | Diffraction
UHF | 300MHz - 3GHz | 10cm-100cm | Cellular telephony (GSM, NMT, AMPS), digital TV, fixed point-to-point, satellite, radar | Shadowing by mountains and buildings
SHF | 3GHz - 30GHz | 1cm-10cm | Broadband indoor systems, Microwave links, satellite. | Attenuation due to rain, snow and fog
EHF | 30GHz - 300GHz | 1mm-10mm | LOS communication (short distance or satellite) | Attenuation due to rain, snow and fog
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 12: Radio Transmitters
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 13: AM Radio Transmitter using High Carrier Power Level
Master Oscillator
Buffer Amplifier
Harmonic Generator
Class C Power Amplifiers
Modulated Amplifier
Modulating Amplifier
Audio Amplifiers
Modulating Signal
Transmitting
Antenna
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 14
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 15: Terrestrial propagation of EM Waves
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 16: AM Radio Transmitter using Low Carrier Power Level
Power Amplifiers
Master Oscillator
Buffer Amplifier
Harmonic Generator
Modulated Amplifier
Modulating Amplifier
Modulating Signal
Transmitting
Antenna
Class - C
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 17: SSB Transmitter
The Filter Method
Phase Shift Method
Weaver’s Method.
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 18: SSB Transmitter ( Filter Method)
Crystal Oscillator
100 KHz
Balanced Modulator
Band Pass Filter
R F
Power Amplifiers
Transmitting
Antenna
Band Pass Filter
100 KHz
(100.3 – 103.4 KHz)
Band Pass Filter
Second Mixer
First Mixer
R F
Power Amplifiers
Oscillator 2
12 MHz
Oscillator 1
3 MHz
(3.1003-3.1034 MHz)
(15.1003-15.1034 MHz)
Modulating Amplifier
(Modulating Voltage
300Hz-3.4KHz)
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 19: Radio Telegraph Transmitter
Interrupted Continuous Wave (ICW) type or ON-OFF keying type.
Modulated Continuous Type (MCT) type.
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 20: Radio Telegraph Transmitter (ON-OFF Keying)
Class C
Power Amplifiers
Crystal Master Oscillator
Buffer Amplifier
Harmonic Generator
Modulator
Modulating D.C.
Telegraph Signal
Transmitting
Antenna
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 21: FM Transmitters
Frequency Modulation
Direct Methods
FM using Reactance tube
FM using Reactance FET
FM using Reactance BJT
FM using Reactance VaractorDiode
Indirect Methods
Predistorting
Armstrong Modulator
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 22: FM Transmitter using Reactance Modulator
AF Voltage Amplifier
Pre-emphasis Circuit
Reactance Tube
Oiscillator
Fc
Modulating
Signal
(50Hz to
15KHZ)
Transmitting
Antenna
Buffer Amplifier
Three Frequency Doublers
Frequency Tripler
R F
Power Amplifier
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 23: Capacitance Reactance Tube Modulator
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 24: Frequency Doubler.
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 25: Armstrong FM Transmitter
Carrier Amplifier
Buffer Amplifier
Crystal Oscillator
(200KHz)
Combining Filter
900
Phase Shift
Balanced Modulator
Pre emphasis
Predistorter
Audio Amplifier
Six Doublers
Frequency Changer
Frequency Multipliers
R F Power Amplifier
Crystal Oscillator
Modulating Voltage
Transmitting Antenna
11.807 MHz
25 x 3
T Srinivasa Rao
<number>
Communication Systems (EC-326)

## Slide 26: Next… Radio Receivers…
T Srinivasa Rao
<number>
Communication Systems (EC-326)